## Slide 1
MPLS Traffic test with xGenius
Guide & Slides corresponding to software ver. 2.3.13
MPLS Traffic test

## Slide 2: Zeus & xGenius
Zeus & xGenius provide deep insights to design, install, maintain, troubleshoot and engineer communications resources of Mobile Operators, Power Utilities, Finace, Labs and R+D centers. The unit is able to verify Ethernet/IP, SyncE, PTP, GbE, IRIG-B, 1PPS, T1/E1, G703, Serial Datacom, C37.94, GOOSE, SV, MMS, Round-trip & One-way Delay tests at all interfaces.
It also has a set of programmable filters to capture live data traffic at wire-speed

## Slide 3: Interfaces & time References
xGenius generates and analyses different kinds of 1544 kb/s and 2048 kb/s signals and also unframed 1544 / 2048 kb/s signals.
PHM
RJ45-C
BNC-C
SFP+ A
SFP+ B
RJ45-A
RJ45-B
SFP-A
Micro SD
SMB-2
SMB-1
SMA
SMB-C
RJ45
SFP-B
 | GNSS | Eth/IP | PTP | NTP | ToD | IRIG-B | PPS | PP2S | SyncE | T1/E1 | MHz | Data
RJ45-A |  | in/out | in/out | in/out |  |  |  |  | in/out |  |  | 
RJ45-B |  | in/out |  |  |  |  |  |  | in/out |  |  | 
SFP-A |  | in/out | in/out | in/out |  |  |  |  | in/out |  |  | 
SFP-B |  | in/out |  |  |  |  |  |  | in/out |  |  | 
SFP+A |  | in/out | in/out | in/out |  |  |  |  | in/out |  |  | 
SFP+B |  | in/out |  |  |  |  |  |  | in/out |  |  | 
BNC-C |  |  |  |  |  |  |  |  |  | in/out | in/out | 
RJ45-C |  |  |  |  | in |  | in | in |  | in/out | in/out | 
SMB-C |  |  |  |  |  |  |  |  |  |  |  | 
SMA | in |  |  |  |  |  |  |  |  |  |  | 
SMB-1 |  |  |  |  |  | in | in | in |  |  |  | 
SMB-2 |  |  |  |  |  | out | out | out |  |  |  | 
RJ-45 |  |  |  |  | in/out | in/out | in/out | in/out |  | in/out | in/out | 
PHM |  |  |  |  |  |  |  |  |  |  |  | in/out

## Slide 4: The MPLS label format
When Ethernet is used as the transport infrastructure, it is necessary to add a header between the IEEE 802.3 MAC frames and the IP header to carry the MPLS label. The label format is shared by MPLS flavors and profiles: IP/MPLS, VPLS, MPLS-TP…

## Slide 5: The Traffic test
The test described aims to teach how to set up the tester to generate and receive real traffic with specific frames, bit rates, and events. With a few changes it will be possible to evaluate other traffic parameters such as throughput, latency, frame loss rate, etc. The document also describes specific formats for tracing and reporting the results of this test.
MPLS
1
ALBEDO
xGenius
Port A
Port B

## Slide 6: Connecting the BNC cables to Port C
xGenius Ports A and B have the connector for the RJ45 cables
xGenius also support optical media and higher bit rates but we are going to execute this test in 1000BASE-T
Connect the Cable to Port A
Connect the Cable to Port B
1
1

## Slide 7: Select the global operation mode
Restore defaults: Home > [System] > Reset to factory settings := Yes
Set operation mode: Home > Config > Mode := IP endpoint (Mind that we have IP otherwise we would need a proper MPLS-TP mode)
It is very important to understand the following steps, that we have to setup separately several layers including: PHY, MAC, IP, & MPLS layers
And we have to setup two ports: A & B ports
2
1

## Slide 8: Configure the PHY layer
Configure in Tester the Physical layer:
Config > Port A > Port Mode := Tx/Rx
Config > Port A > Physical Layer > Connector := Electrical
Configure also Tester Port B in the same way than Port A:
Config > Port B > Port Mode := Tx/Rx
Config > Port B > Physical Layer > Connector := Electrical
2
1

## Slide 9: Configure the MAC layer
Configure in Tester the MAC layer:
Config > Port A > Frame Layer > Flow A1 > Frame size := 1280
Config > Port A > Frame Layer > Flow A1 > Dest MAC address from := ARP
2
1

## Slide 10: Configure the IP layer
Configure in Tester Port A local profile:
Config > Port A > Local profile > Use DHCP := No
Config > Port A > Local profile > Static IPv4 address := 10.10.10.1
Config > Port A > Local profile > Static IPv4 network mask := 255.0.0.0
Configure also Tester Port B local profile:
Config > Port B > Local profile > Use DHCP := No
Config > Port B > Local profile > Static IPv4 address := 10.10.10.2
Config > Port B > Local profile > Static IPv4 network mask := 255.0.0.0
3
2

## Slide 11: Configure the MPLS layer
Configure in Tester the MPLS stack:
Config > Port A > MPLS > Flow A1 > Stack Configuration := Single MPLS label
Config > Port A > MPLS > Flow A1 > Bottom label := 1001
2
1

## Slide 12: Configure the IP layer
Configure in Tester the destination IP address to be the Port B address:
Config > Port A > Network Layer > Flow A1 > Destination address from := Port B
3
1

## Slide 13: Configure Traffic Profile
The tester can generate up to 8 traffic flows simultaneously, set up the 1st one:
Config > Port A > Bandwidth profile > Flow A1 := Ramp
Configure the bandwidth parameters:
Config > Port A > Bandwidth profile > Flow A1 > Transmission rate := [Rate fr/s | Rate (Mb/s) | Rate (%) …]
Program the payload to a PRBS: Config > Port A > Payload > Flow A1 > Payload type := BERT Config > Port A > Payload > Flow A1 > BERT patterns := ITU PBS 2^11
Set the payload in Port B, flow B1 in the same way.
2
1

## Slide 14: Press RUN
You can spot the frame and the test profile configured at Flow A1 including the type of traffic to be generated at Port A including the flow, the Physical layer, the Ethernet frame, MAC addresses, the PRBS generated, etc.
Make sure that Filter B1 is configured to match the traffic from Port A Config > Port B > Filters > Filter B1 > Filter mode := Match port A
Press RUN to activate the traffic generation
1
2

## Slide 15: Press RUN
You can see now you are receiving MPLS labels from the following menu:
Results > Port B > MPLS statistics
Press LED symbol and select Port B
Immediately the RX LED will turn green indicating the reception of traffic
As you have selected a PRBS spot the LED indicating that the pattern is being received correctly
2
3
4
1
5

## Slide 16: Press RUN
You can see now you are receiving MPLS labels from the following menu:
You can spot other results for instance some statistics regarding traffic: Results > Port B > Bandwidth statistics > General statistics
1

## Slide 17: Insert events in Tester 1
2
5
This is a good practice to understand how it all works
Test > Insertion > Insert to := Port A
Test > Insertion > Event to insert := TSE
Test > Insertion > Mode := Single
Press Event to insert one TSE error
Spot how the error appears in the LED and the tester shows an E label
4

## Slide 18: Event logger enable
Global counts, statistics and LEDs provide information about which events and how many of them have been registered but they do not say too much about how they are distributed in time. These information is supplied at the Event Logger a graphical representation tool that permits to trace the evolution of key parameters. The first thing to to is to enable it:
Stop the tester
Home > Test > Event logger sep > Enable := Yes
Clear the currently selected filtertus: Clear all filters := Yes
1
2
3

## Slide 19: Select the Events to Log
Now you need to select which events you want to trace are categorized in classes:
Test > Event Logger setup > [ Port A | Port B | System event | Debug events]
You will find out several groups of events and statistics: Port A event filter := [Anom/defts | Bwd | Frame | SLA | BERT]
For our particular test select a bundle or events in Port A : Port A event filter > Bandwidth stats > Filter A1 := [Ethernet | IPv4 | IPv6 | UDP]
1
3
2
2
1
3

## Slide 20: Display the logs
With the Event Logger you can select one or various events and trace them so that all changes along with the time and date these changes are registered are recorded with a 1 second resolution. The event logger provides representations and zoom levels to enable event analysis at different time scales:
Go to Results > Event logger
To select a saved trace double click at (…) to display the folder of traces
Select and Open one of the files
1
2
3
3

## Slide 21: Display chronogram & histogram
To display the logger open the actual trace always in red
Select the event you want (double click) to display in the chronogram
You can see the value evolution
To know the exact value at one specific moment press on the screen
Mind that you can see both Port A and Port B
1
3
4
4
5

## Slide 22: Scale the results on screen
You can change the scale to see in more details the results
Using the auxiliary bars change the vertical scale
Reset to the original scale
2
3
1

## Slide 23: Exporting Logs
To export log files in CSV format:
Go Home > [File icon] > Configuration files | Report files > Internal memory to list the files currently stored in the unit
Select the files you want to export: File name > Export
Choose an external device: micro SD | USB
If no external device a popup will appear: ‘No devices present’
2
3
1
1

## Slide 24
That’s all
www.albedotelecom.com